Week 1 + 2
Research Linear displacement sensors

Types of sensors:
- Linear Variable Differential Transformers (LVDT)
- Ultrasonic
- Lasers
- Potentiometers
- Magnetic sensors

LVDTs:
- Linear Variable Differential Transformer
- Hollow inductor coil with rod that pushes inside, output changes based on rod position
- Infinite analog resolution (resolution is as good as ADC allows)
- More accurate ones require AC power supplies and give AC output
  - AC supply, DC output exist, so do DC/DC
  - Tradeoff is in accuracy or price
- I have been unable to locate an LVDT with digital output
- Ranges up to a few inches, one inch range is fine

Ultrasonic:
- Transducer generates signal output, receiver catches echo and calculates distance
- Generally tuned for either really long or really short distances
  - Tough to find in the 1 inch range
- Less accurate than LVDT

Lasers
- High precision
- Suitable for 1 inch range
- Expensive

Potentiometers
- Sliding contact on a rod used as a voltage divider
- Easy to incorporate into designs
- Not very accurate
- Subject to mechanical wear

Magnetic sensors (Hall effect)
- Place a magnet on device, place a receiver from measurement point, measure strength of field
- Limited range (most could be too short for our purposes)

http://www.machinedesign.com/sensors/finding-right-sensor-linear-displacement is a decent reference

For this project, I have come to the conclusion that LVDTs are the most likely sensor. Lasers are too expensive, and other sensors lack the required resolution. The draw back is that LVDTs require support electronics. At the very minimum an ADC will be required; potentially a characterizing circuit will be necessary, and at worst case an AC power supply as well. They also vary widely in price, but we're probably looking at between $400 and $1000.
I have not ordered any sensors, and am slightly behind schedule in that regard. It has taken longer to identify appropriate sensors than anticipated. At the resolution required (10-4 inches), it is difficult to find a sensor that
- Is precise enough
- Requires minimal electronics to read values from
- Is relatively inexpensive
Suitable devices are manufactured with industry in mind. I will not be using a PLC, disqualifying some sensors as they are built with PLC's in mind. It is also takes time to find the price of sensors; everyone wants me to ask for a quote, and some reply faster than others.

I have come to the conclusion that a PCB with some supporting devices will be required. I need to continue my efforts to find a suitable sensor, now knowing that I'm not getting away with avoiding PCB design.

Additionally I need to identify a pressure sensor still. This will be relatively easy, as it does not need to be precise. The application we need it to fulfill falls within the range of hobby electronics used by amateur enthusiasts, and there is a wide range of devices with existing libraries and documentation.

A simple block diagram is shown below of the intended design architecture.

With future projects in mind, I have decided to target the Raspberry Pi Zero W as my controller. If future laboratory equipment is updated to use IoT devices, another Pi can be used. Each device costs ~$10, and has extensive documentation, guides, and existing code libraries for any purpose one could desire. Additionally, it will allow reuse of the database; code from this project could be reused to log data from arbitrary new sensors.

The Pi Zero W includes a 2.4 Ghz Wifi module. It will communicate with the existing Wifi in the soil lab, which will allow access to a database hosted using CITS' existing software (Probably some variant of mySQL). Sensors will communicate with the Pi through a custom designed PCB with at the very least an analog to digital converter (ADC).

This project is being documented on Github. Any of the files I use can be located at https://github.com/RichardMuri/Civil_IoT.